## Slide 1
Lab 6: Virtual LAN (VLANs)
Course: Computer Networks
Prepared by: Hajra Batool

## Slide 2
Objectives
Create and configure VLAN 10 and VLAN 20 in Cisco Packet Tracer
Assign switch ports to different VLANs
Understand and configure Router on a Stick
Configure Native VLAN
Identify and fix Native VLAN mismatch

## Slide 3
What is a VLAN?
VLAN stands for Virtual Local Area Network.
It logically divides one physical switch into separate networks.
Each VLAN creates a separate broadcast domain.
Devices in different VLANs cannot communicate directly without routing.
VLANs improve organization, management and network security.

## Slide 4
VLANs Used in This Lab
VLAN 10 → Voice
VLAN 20 → Sales
Giving VLANs meaningful names makes administration easier.
Names can represent departments or network roles.
Example: Voice, Sales, Marketing, HR, IT.

## Slide 5
Creating VLANs
Enter configuration mode:
Switch(config)# vlan 10
Switch(config-vlan)# name Voice
Switch(config)# vlan 20
Switch(config-vlan)# name Sales
Verify with: show vlan brief

## Slide 6
Verifying VLANs
Command: show vlan brief
Displays VLAN ID and VLAN name.
Also shows the switch ports assigned to each VLAN.
Newly created VLANs normally have no access ports assigned until we configure them.

## Slide 7
Assigning a Port to VLAN 10
Select the interface:
Switch(config)# interface fastEthernet 0/1
Set it as an access port:
Switch(config-if)# switchport mode access
Assign VLAN 10:
Switch(config-if)# switchport access vlan 10

## Slide 8
Assigning Multiple Ports to VLAN 20
Use interface range to configure several ports together:
Switch(config)# interface range fastEthernet 0/2 - 6
Switch(config-if-range)# switchport mode access
Switch(config-if-range)# switchport access vlan 20
This avoids repeating the same commands for every port.

## Slide 9
Port Assignment Summary
Fa0/1 → VLAN 10 (Voice)
Fa0/2–Fa0/6 → VLAN 20 (Sales)
Access ports carry traffic for one VLAN.
By default, switch ports belong to VLAN 1.
Use show vlan brief to verify assignments.

## Slide 10
Why Inter-VLAN Routing?
Each VLAN represents a separate network/subnet.
VLAN 10 and VLAN 20 are isolated at Layer 2.
A router or Layer 3 switch is required for communication between VLANs.
Example: A Sales PC in VLAN 20 needs routing to communicate with a Voice PC in VLAN 10.

## Slide 11
Router on a Stick
Router on a Stick enables routing between multiple VLANs using one physical router interface.
The router interface is divided into logical sub-interfaces.
Each sub-interface receives an IP address for a different VLAN.
The switch-to-router link must be configured as a trunk.
This saves physical router and switch interfaces.

## Slide 12
Router on a Stick: How It Works
Switch receives traffic from VLAN 10 or VLAN 20.
The trunk carries traffic for multiple VLANs to the router.
Router sub-interface identifies the VLAN using 802.1Q tagging.
The router routes traffic between the VLAN networks.
The packet returns through the trunk to the destination VLAN.

## Slide 13
Router Sub-Interfaces
Example for VLAN 10:
Router(config)# interface g0/0.10
Router(config-subif)# encapsulation dot1Q 10
Router(config-subif)# ip address 192.168.10.1 255.255.255.0
Example for VLAN 20:
Router(config)# interface g0/0.20
Router(config-subif)# encapsulation dot1Q 20
Router(config-subif)# ip address 192.168.20.1 255.255.255.0

## Slide 14
Default Gateway Configuration
Each end device must use the router sub-interface as its default gateway.
VLAN 10 PCs → Gateway 192.168.10.1
VLAN 20 PCs → Gateway 192.168.20.1
The gateway forwards traffic when the destination is in another network.
Test connectivity with ping.

## Slide 15
Configure the Switch Trunk
The switch port connected to the router must carry multiple VLANs.
Example:
Switch(config)# interface gigabitEthernet 0/1
Switch(config-if)# switchport mode trunk
The trunk allows VLAN 10 and VLAN 20 traffic to reach the router.
Verify using: show interfaces trunk

## Slide 16
Alternative: Separate Router Interfaces
Inter-VLAN routing can also be configured using separate physical interfaces.
Each VLAN requires a separate router/switch connection.
This consumes more physical interfaces.
It becomes inefficient when many VLANs are present.
Router on a Stick solves this by using one physical router interface with multiple sub-interfaces.

## Slide 17
Layer 3 Switch Alternative
A Layer 3 switch can perform routing between VLANs.
Create a Switch Virtual Interface (SVI) for each VLAN.
Assign an IP address to each SVI.
The switch performs routing between VLANs.
Layer 3 switches are powerful but can be more expensive than basic switches.

## Slide 18
What is Native VLAN?
Native VLAN is the VLAN assigned to untagged traffic received on a trunk.
802.1Q trunks normally tag VLAN traffic.
Native VLAN traffic is carried without a VLAN tag.
By default, Cisco switches use VLAN 1 as the native VLAN.
The native VLAN should be configured consistently on both ends of a trunk.

## Slide 19
Why Do We Need Native VLAN?
Some devices cannot add VLAN tags to their traffic.
Examples include legacy hubs and certain end-device connections.
Untagged traffic arriving on a trunk is placed into the configured native VLAN.
Native VLAN can also be used with IP phone + PC daisy-chain scenarios.
The key point: untagged traffic must have an agreed VLAN on the trunk.

## Slide 20
Configuring Native VLAN
Example:
Switch(config)# interface gigabitEthernet 0/1
Switch(config-if)# switchport trunk native vlan 10
The native VLAN becomes VLAN 10 on that trunk interface.
Configure the same native VLAN on the other end of the trunk.

## Slide 21
Native VLAN Mismatch
A native VLAN mismatch occurs when the two ends of a trunk use different native VLANs.
Example:
Switch A native VLAN → 10
Switch B native VLAN → 20
This causes untagged traffic to be associated with different VLANs at each end.
Cisco may display a native VLAN mismatch warning.

## Slide 22
How to Detect a Mismatch
Use:
show interfaces trunk
Check the Native VLAN column on both trunk interfaces.
Compare the native VLAN configured on each side.
Also check switch messages/warnings for native VLAN mismatch.

## Slide 23
Fixing Native VLAN Mismatch
Choose one native VLAN for the trunk.
Configure the same native VLAN on both ends.
Example:
Switch A(config-if)# switchport trunk native vlan 10
Switch B(config-if)# switchport trunk native vlan 10
Verify again with: show interfaces trunk

## Slide 24
Troubleshooting Checklist
1. Confirm VLAN 10 and VLAN 20 exist: show vlan brief
2. Confirm access ports are assigned correctly.
3. Confirm the router link is a trunk.
4. Confirm router sub-interfaces use correct VLAN IDs.
5. Check PC IP addresses and default gateways.
6. Check native VLAN on both trunk ends.
7. Test using ping.

## Slide 25
Complete Lab Flow
Create VLAN 10 → Voice
Create VLAN 20 → Sales
Assign Fa0/1 to VLAN 10
Assign Fa0/2–Fa0/6 to VLAN 20
Configure switch-to-router trunk
Create router sub-interfaces
Configure IP addresses and gateways
Configure/verify Native VLAN
Test inter-VLAN connectivity
VLANs, Router on a Stick & Native VLAN | 26

## Slide 26
Important Commands
show vlan brief → View VLANs and access-port assignments
show interfaces trunk → View trunk and native VLAN information
switchport mode access → Configure an access port
switchport access vlan 10 → Assign an access port
switchport mode trunk → Configure a trunk
switchport trunk native vlan 10 → Set native VLAN
encapsulation dot1Q 10 → Map sub-interface to VLAN 10
VLANs, Router on a Stick & Native VLAN | 27